The Toughest Multimeters

FEATURES :

APPA 103N APPA 105N APPA 106 APPA 107 APPA 109 Main Display 4000 Count 4000 Count 4000 Count 20000/4000 Count 20000/4000 Count Dual Digital Display NA NA NA Analog Bar graph Display 82 segments 82 segments 82 segments 83 segments 83 segments Zoom Analog Bar graph NA NA NA Center Zero Analog Bar graph NA NA NA Self-Calibration NA NA NA True RMS NA NA True RMS AC+DC True RMS AC+DC True RMS Data Hold NA NA Auto Hold NA NA NA Relative Mode NA Min/Max/Avg Function NA Peak Hold NA Store, Recall Function NA NA NA Up to 1000 records Up to 1000 records oC/oF Temperature Test NA NA Auto Fuse Detector NA NA NA Beep Guard NA NA NA RS - 232 Cable OPTION OPTION OPTION OPTION INCLUDED WinDMM 100J software OPTION OPTION OPTION NA NA WinDMM 100 software NA NA NA OPTION INCLUDED Data logger records NA NA NA 6,000 records 40000 records dBm/ dB measurement NA NA NA Continuity Check/Beeper Low Voltage Ohms NA NA NA Backlight Open Communication Protocol Water / Dust Resistant High Energy Fuses Protective Holster

SPECIFICATIONS: (All at 23oC 5oC, < 80% R.H.)

APPA 103N APPA 105N APPA 106 APPA 107 APPA 109 DCV: Ranges 400mV ~ 1000V 400mV ~ 1000V 400mV ~ 1000V 20mV ~ 1000V 20mV ~ 1000V Resolution 0.1mV 0.1mV 0.1mV 0.001mV 0.001mV Basic Accuracy (0.25%+1d) (0.1%+1d) (0.1%+1d) (0.06%+10d) (0.06%+10d) ACV: Ranges 400mV ~ 750V 400mV ~ 750V 400mV ~ 750V 20mV ~ 750V 20mV ~ 750V Resolution 0.1mV 0.1mV 0.1mV 0.001mV 0.001mV Basic Accuracy (1.3%+ 5d) (1.0%+ 5d) (1.0%+ 5d) (0.70% + 50d), 40Hz ~ 100Hz (0.70% + 50d), 40Hz ~ 100Hz Bandwidth 40Hz ~ 1KHz 40Hz ~ 1KHz 40Hz ~ 1KHz 40Hz ~ 50KHz 40Hz ~ 100KHz Ranges 400 ~ 40M 400 ~ 40M 400 ~ 40M 200 ~ 2G 200 ~ 2G Resolution 0.1 0.1 0.1 0.01 0.01 Basic Accuracy (0.6%+ 2d) (0.4%+ 2d) (0.4%+ 2d) (0.30% + 30d), 200 ~ 200K (0.30% + 30d), 200 ~ 200K DIODE TEST: Test Current 1.5mA (Typical) 1.5mA (Typical) 1.5mA (Typical) 1.1mA (Typical) 1.1mA (Typical) Open circuit voltage 3V DC (max). 3V DC (max). 3V DC (max). 3.3V DC (max). 3.3V DC (max). Continuity Test: Threshold Approx.30 Approx.30 Approx.30 Approx.50 Approx.50 Indicator 2KHz Tone Buzzer 2KHz Tone Buzzer 2KHz Tone Buzzer 2KHz Tone Buzzer 2KHz Tone Buzzer DCA: Ranges 40mA ~ 10A 40mA ~ 10A 40mA ~ 10A 20mA ~ 10A 20mA ~ 10A Resolution 10A 10A 10A 0.001mA 0.001mA Basic Accuracy (0.6%+ 2d) (0.4%+ 2d) (0.4%+ 2d) (0.20%+ 40d) (0.20%+ 40d) ACA: Ranges 40mA ~ 10A 40mA ~ 10A 40mA ~ 10A 20mA ~ 10A 20mA ~ 10A Resolution 10A 10A 10A 0.001mA 0.001mA Basic Accuracy (1.3%+ 5d) (1.3%+ 5d) (1.3%+ 5d) (0.80%+ 50d), 40Hz ~ 500Hz (0.80%+ 50d), 40Hz ~ 500Hz Bandwidth 40Hz ~ 1KHz 40Hz ~ 1KHz 40Hz ~ 1KHz 40Hz ~ 3KHz 40Hz ~ 3KHz Capacitance: Ranges 4nF ~ 40mF 4nF ~ 40mF 4nF ~ 40mF 4nF ~ 40mF 4nF ~ 40mF Resolution 1pF 1pF 1pF 1pF 1pF Basic Accuracy (2%+ 5d) (2%+ 5d) (2%+ 5d) (0.90%+ 5d), 400nF ~ 4F (0.90%+ 5d), 400nF ~ 4F Hz: Ranges 4KHz ~ 40MHz 4KHz ~ 400MHz 4KHz ~ 400MHz 20Hz ~ 1MHz 20Hz ~ 1MHz Resolution 1Hz 1Hz 1Hz 0.01Hz 0.01Hz Basic Accuracy (0.01%+ 1d) (0.01%+ 1d) (0.01%+ 1d) (0.01%+ 10d) (0.01%+ 10d) RPM: Ranges 40KRPM ~ 400KRPM 40KRPM ~ 400MRPM 40KRPM ~ 400MRPM NA NA Resolution 30RPM 30RPM 30RPM Basic Accuracy (0.01%+ 10d) (0.01%+ 10d) (0.01%+ 10d) %DF: Ranges NA NA NA 20% ~ 80% 20% ~ 80% Resolution 0.1% 0.1% Basic Accuracy 1% ( 20Hz ~ 10KHz, 5Vp-p ). 1% ( 20Hz ~ 10KHz, 5Vp-p ). Temperature: Ranges NA NA -20oC ~ 800oC -200oC ~ 1200oC -200oC ~ 1200oC Resolution 1oC 0.1 oC 0.1 oC Basic Accuracy (2%+ 4oC), -20oC ~ 350oC (2%+ 2oC), 350oC ~ 500oC (3%+ 2oC), 501oC ~ 800oC (0.1%+6oC), -200oC ~ 100oC (0.1%+3oC), 100oC ~ 1200oC (0.1%+6oC), -200oC ~ 100oC (0.1%+3oCs), 100oC ~ 1200oC

GENERAL SPECIFICATIONS:

APPA 103N APPA 105N APPA 106 APPA 107 APPA 109 Sampling Rate: 2.5times/sec Auto Power Off: 30 minutes Operating Temperature: 0oC ~ 50oC Storage Temperature: -20oC ~ 60oC 0 to 80% R.H. Temperature: Coefficient: 0.15x(Spec.Sccuracy)/oC, <18oC, >28oC Safty Standard: IEC 61010 & designed to meet UL3111 specifications. CAT. III 600V, CAT. II 1000V. CAT. III 600V, CAT. II 1000V. CAT. III 600V, CAT. II 1000V. CAT. III 600V, CAT. II 1000V. CAT. III 600V, CAT. II 1000V Battery Life: in hours ( Alkaline battery ) 450 450 300 100 100 Power Requirement: Single 9V battery (NEDA 1604 or IEC 6F22 ) NA NA IEC, LR03, AM4 Aor AAA Size 1.5 x2 NA NA NA Dimensions: 86mm (W) x 185mm (L) x 31.5mm (D) 98mm ( W ) x 197mm ( L ) x 50mm ( D ) with holster Weight: in grams (with holster) 620 620 620 620 620 Accessories: Protective holster, test leads, test clips, ZnC battery (installed) and manual. Protective holster, test leads, test clips, ZnC battery (installed) and manual. Protective holster, test leads, test clips, Temp. adaptor, Bead sensor, Alkaline, battery (installed) and manual. Protective holster, test leads, test clips, Temp. adaptor, Bead sensor. Alkaline battery (installed) and manual. Protective holster, test leads, test clips, Temp. adaptor, Bead sensor. Alkaline battery (installed) and manual. Optical RS 232 Cable: OPTION OPTION OPTION OPTION INCLUDED APPA WinDMM 100J software: OPTION OPTION OPTION NA NA APPA WinDMM 100 software: NA NA NA OPTION INCLUDED